## Slide 1: UMRT Arduino Workshop
E2-351 6pm-7:30pm 2026-04-02 Quinn Gibbons & Quinn Thiessen

## Slide 2: Schedule
Arduino 101
What is the Arduino & some of it's uses
Basics of Arduino
Connecting components
Setup
Downloading the IDE
Board and Port selection
Installing Libraries
Coding 101
Basics of the Arduino IDE
Setup of setup
Important Functions
Quick Project
We will do a simple project together
Future Resources / Advice
Kits to buy & Resources for future learning
Last bits of Advice
You will have time to try your own variations

## Slide 3: Downloading the IDE
Go to this website: https://docs.arduino.cc/software/ide/
(on your laptop)
Setup
Notes: Laptop charged
USB type A port
Ardunio IDE installed

## Slide 4: What is the Arduino?
Arduino 101
The hardware:
A variety of microcontrollers with unique functions, allowing you to connect to and control real world components.
The software:
The Arduino IDE uses a language similar to C++.
The community:
Everything is open source, meaning offbrand boards can legally be reproduced by anyone. This also means there is a massive shared library for Arduino components as a resource.

## Slide 5: Somethings you can do...
Arduino 101

## Slide 6: Basics of the board
Arduino 101
Digital pins
Power pins
Analog pins
Note: if they have a ~, they are capable of pulse width modulation (PWM)
I2C Communication pins
Reference pins
Reset pin

## Slide 7: Powering the Arduino
It is recommended to power the Arduino via USB port to your computer
Arduino 101
USB port (5V)
DC Barrel Jack (7-12V)
Vin port (7-12V)

## Slide 8: Breadboard
NOTE: If you are using motors and high power consumption components, make sure you are careful with power ratings + consumption!!!
The breadboard will allow you to build circuits without soldering.
Typically you use the long rows as power and ground
Keep in mind rows are linked horizontally, and do not cross the middle divider
There is also no connection from upper to lower rows
Arduino 101

## Slide 9: Some common components:
Motors
Sensors
LEDs
Potentiometers / Switches / Buttons
Buzzers
Arduino 101

## Slide 10: Board + Port Setup
To choose a port go to
  Tools > Port > [select the port your arduino is connected to]
To choose a board go to
  Tools > Board > Arduino AVR Boards > Arduino Uno
(Or alternately select both from this dropdown)
Setup

## Slide 11: FYI: Installing Libraries
Libraries: Prebuilt code. They can provide specific functions for individual Arduino components.
You can either install zip libraries or select in the Library Manager
Setup

## Slide 12: Basics of the Arduino IDE
Coding 101

## Slide 13: Basics of the Arduino IDE
The IDE uses a language similar to C++
Every program:
  Setup function
  Loop function
Order of execution:
  Setup()
  Loop()
  Loop()
  Loop()
  …..
Coding 101

## Slide 14: Basics of the Arduino IDE
Coding 101

## Slide 15: Basics of the Arduino IDE
Coding 101
Plug in servo:
  Ground (Brown)
  5V
  Data (pin 3)
Run the code
Keep the servo plugged in

## Slide 16: Questions?
We will be moving on to the small project next.
Coding 101

## Slide 17: The project
First, a short video about the components.
https://www.youtube.com/watch?v=KGwtit2bFyo
We will not be making the project in the video together.
The project

## Slide 18: The project (pt. 1/2): Distance detection
We will start from the "Blink" example!
  Connect the ultrasonic sensor
  Set up Serial printing ("Hello, World")
  Read and print the distance value
The project

## Slide 19: The project (pt. 2/2): Distance Controlled Motor
Copy the code from 'Sweep' to set up the servo
Make sure your servo is still plugged in
Add the line of code:
  myServo.write(distance)
  You're done!
The project

## Slide 20: Big Example

## Slide 21: Code for all previous parts
https://github.com/UMRoboticsTeam/arduino-workshop-April-2026/

## Slide 22: Short additions to this project If we have time... Try one!
Easy:
  Make the built-in LED turn on if the distance is close enough
  If you've done that: Make an array of LEDs turn on one at a time the closer you get
Medium:
  Modify the 'Sweep' code to change the speed depending on the distance
Hard:
  Plug in the 'joystick' and use it to control the servo
    The joystick resting position should keep the servo still
    Left/right should control the servo
  Note: The joystick has two potentiometers! Use analog read.
The project

## Slide 23: Here are some resources to help you in the future
Tinkercad: https://www.tinkercad.com/ : Free simulation
These are some websites with premade projects:
  https://projecthub.arduino.cc/
  https://www.instructables.com/
Our good friend Chat
Starter kit [50$]: https://a.co/d/09PPf3wS
Future resources

## Slide 24: Tips from the '''expert'''
VS Code Extension called "PlatformIO" lets you program Arduinos
  This way you don't need the Arduino IDE. (look up a tutorial)
ESP32 is (basically) Arduino with WiFi/bluetooth (wireless)
If you buy pre-made sensors (like AdaFruit) they may have a library
The Arduino examples are helpful to
  See the correct syntax
  Straight up copy
  See how to use a specific library / tool (like a servo)
Future resources

## Slide 25: Tips from the '''expert'''
  Helpful for the language
Future resources

## Slide 26: Tips from the '''expert'''
  Three categories of examples:
    Built in For YOUR board For YOUR libraries
    (most basic) (can be quite specific) (you install; very specific)
Future resources

## Slide 27: Thanks for joining us in the workshop!
You guys since you joined the workshop
If you have further questions, feel free to contact either of us on discord!!